## Slide 1: Anterior Vitrectomy
Stephen Lash BM, BSc (Hons), MCOptom, FRCOphth, MBA
Consultant VR Surgeon
University Hospital Southampton

## Slide 2: First things first with vitreous loss
Stop
Keep Calm
Ensure patient comfortable and explain it may take a little bit longer
Get the kit sorted
Wait and think!

## Slide 3: Visualise
Spend time thinking through what you would do and rehearse this over and over again in real time in your head!
When it happens it will therefore not be your first time!

## Slide 4: Flow
Forget bottle height / aspiration /Vacuum/etc etc
Use existing wounds unless they are very leaky and then consider a half width paracentesis
GET THE FLOW FORM FRONT TO BACK NOT FROM BACK TO FRONT
  Infusion in the AC
  Cutter through the hole in PC and down into the vitreous focused right down on the microscope
  Fluid will now flow backwards
  If the cutter is in the AC fluid will pass into the gel (Hydrate it and stir it up) and gel will move forward into AC and into the cutter.
  Cutter back and cavitate the central gel
  Gel will fall back with flow

## Slide 5: Cutter
Fluid on Simcoe or green needle with enough flow rate to keep globe formed. Just into AC
Cutter into vitreous through the hole in th ePC and as far back as you can focus
Foot down. Cut rate usually set and at rates up to several thousand. Eye should remain pressured. If it collapses ease off the foot, increase the fluid flow.
Cavitate the gel. It is not a magic wand so avoid waving it around! This pulls on the gel.
Keep cutter still, allow gel to come to cutter.
When gel stops, slowly rotate and start again until 360 degrees cleared.
Cavitate Gel

## Slide 6: Vitreous
Difficult to see
Consider a drop of washed IVTA to highlight gel
When gel cavitated check wounds. If strands they may be free and come out with no traction. If they are attached do not chase in the AC go back through the PC
Cavitate some more
Check again
CLEAR GEL

## Slide 7: Cutter caution
Easy to nibble the capsule, back OK but leave anterior intact (?optic capture lens)
Easy to nibble the iris (Stay away!)
Keep calm, Keep still

## Slide 8: Lens?
If gel cleared I am happy for you to put lens in sulcus (3 piece, change biometry, reduce power 0.5-1.5 (depending on refractive error)
Optic capture if possible as very stable
Miochol
Final check of wounds ?Suture (depends on wounds!)

## Slide 9: Post op
Maxidex QDS plus (depends how traumatic!)
Chloramphenicol
Pressure?
Explain to patient thoroughly
Take responsibility and ensure you follow up
Warn about flashes and floaters